## Slide 1
Petrol vs. EV
A comparative energy consumption and cost study
February 2012

## Slide 2
CO2 emissions per km
Current Vic. 1080 g/kWh
Current National Average (2017) 820 g/kWh
Estimated 2020 National Average 663 g/kWh
Petrol includes 7.6% upstream emissions factor (NGA)
Chart: g/km CO2
| Freeway | Free urban road | Taxi Run | Outer Urban Commute | Hill Climb | Combined
Petrol | 185.61 | 200.4588 | 264.8036 | 232.6312 | 257.3792 | 233.8043
EV on Vic power 2017 | 236.4596 | 184.275 | 210.8427 | 198.7398 | 212.8859 | 207.3959
EV on NEM 2017 | 179.5342 | 139.9125 | 160.0843 | 150.895 | 161.6356 | 157.4672
EV on NEM 2020 | 145.1599 | 113.1244 | 129.434 | 122.0042 | 130.6883 | 127.318

## Slide 3
Energy cost per km
Petrol high price 144 c/l
Petrol low price 117. c/l
Electricity high price 26.63 c/kWh (domestic peak 2017)
Electricity low price 12.77 c/kWh (domestic off-peak 2017)
*Petrol prices based on Australian Institute of Petroleum over the last 6 months
Chart: Opertaing Cost cents/km
| Freeway | Free urban road | Taxi Run | Outer Urban Commute | Hill Climb | Combined
Petrol Low | 8.775 | 9.477 | 12.519 | 10.998 | 12.168 | 11.0535
Petrol High | 10.875 | 11.745 | 15.515 | 13.63 | 15.08 | 13.6987
EV Low | 2.7959 | 2.1789 | 2.493 | 2.3499 | 2.5172 | 2.4523
EV High | 5.8305 | 4.5437 | 5.1988 | 4.9004 | 5.2492 | 5.1138

## Slide 4
Payback time vs. annual driving distance
Chart: Year after purchase
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
10000 km | -15000 | -13640.696 | -12281.3921 | -10922.0881 | -9562.7842 | -8203.4802 | -6844.1763 | -5484.8723 | -4125.5684 | -2766.2644 | -1406.9605
20 000 km | -15000 | -12781.3921 | -10562.7842 | -8344.1763 | -6125.5684 | -3906.9605 | -1688.3526 | 530.2553 | 2748.8632 | 4967.4711 | 7186.079
30 000 km | -15000 | -11922.0881 | -8844.1763 | -5766.2644 | -2688.3526 | 389.5593 | 3467.4711 | 6545.383 | 9623.2948 | 12701.2067 | 15779.1186
50 000 km | -15000 | -10203.4802 | -5406.9605 | -610.4407 | 4186.079 | 8982.5988 | 13779.1186 | 18575.6383 | 23372.1581 | 28168.6778 | 32965.1976
100 000 km | -15000 | -5906.9605 | 3186.079 | 12279.1186 | 21372.1581 | 30465.1976 | 39558.2371 | 48651.2766 | 57744.3161 | 66837.3557 | 75930.3952

## Slide 5
The grid is only getting greener

## Slide 6
Supporting Information

## Slide 7
Study objectives
What are the real-world operating cost and emissions differences between an electric and petrol-powered vehicle?
How is this affected by driving conditions?

## Slide 8
Comparison methodology
Cars
  MY 13 Holden Calais 3.6L V6
  MY 12 EV Engineering Calais
Driving conditions
  Mixture of urban, city and freeway driving
  Non trained drivers
  Climate control off
Energy Consumption Method
  Petrol – On board trip computer
  Electric – Revenue grade electricity meter

## Slide 9
Test Routes - freeway

## Slide 10
Test Routes – free urban road

## Slide 11
Test Routes – City Taxi

## Slide 12
Test Routes – Country Gents Commute

## Slide 13
Test Routes – Scenic Drive/Hill Climb

## Slide 14
Journey | Start ODO | End ODO | GPS Distance Travelled | Average Speed | Trip Time (hrs) | Max Elevation | Start SOC | End SOC | % of Battery Used
Freeway | 3219 | 3343 | 128.8 | 87.2 | 1.5 | 65 | 92% | 13% | 79%
Free urban road | 3343 | 3499 | 160.0 | 49.2 | 3.3 | 113 | 92% | 18% | 74%
Taxi Run | 3500 | 3638 | 142.4 | 34.1 | 4.2 | 137 | 91% | 13% | 78%
Country gents commute | 3640 | 3776 | 139.7 | 41.9 | 3.3 | 331 | 91% | 18% | 73%
Hill Climb | 3776 | 3897 | 122.8 | 38.7 | 3.2 | 595 | 89% | 20% | 69%
Combined |  |  | 693.6 |  |  |  |  |  | 
Trip summary